## Slide 1
Large-Scale Assessment
of a Smartwatch to Identify
Atrial Fibrillation
Perez et al. · The New England Journal of Medicine · 2019
The Apple Heart Study
419,297 participants · 8 months · Siteless design
1 / 12

## Slide 2
PROBLEM & MOTIVATION
2 / 12
What Is Atrial Fibrillation (AFib)?
How AFib Works
Normal heart: Electrical signals fire in a regular pattern → steady heartbeat
AFib: Electrical signals in the atria become chaotic → heart beats irregularly
Why it's dangerous: Blood pools in the atria → clots can form → clots travel to the brain → stroke
Why it's hard to catch: Often paroxysmal (comes and goes). ECG looks normal between episodes. Can be asymptomatic.
~6M
people in the U.S.
have AFib
5×
increased risk
of stroke
~700K
may be
undiagnosed
1 in 3
lifetime risk
of developing AFib

## Slide 3
PROBLEM & MOTIVATION
3 / 12
The Detection Gap
Current Methods
✕
Standard ECG
Snapshot — misses paroxysmal episodes
✕
Holter Monitor
24-48 hours — too short for infrequent AFib
✕
Implantable Devices
Requires surgery — high barrier
►
What's Needed
✓
Long-term
Monitor for weeks/months, not hours
✓
Passive
No user action required
✓
Non-invasive
No surgery, no prescriptions
✓
Low-barrier
Uses devices people already own
→ Apple Watch + PPG sensor could fill this gap. But can it reliably detect AFib in everyday use?

## Slide 4
STUDY DESIGN
4 / 12
Study Design at a Glance
Prospective
Single-arm
Open-label
Siteless
Pragmatic
Who
419,297 participants
Age ≥ 22, U.S. residents
Own Apple Watch + iPhone
Self-reported: no prior AFib
When
Nov 2017 – Aug 2018
8 months of recruitment
Median 117 days monitoring
End-of-study survey by Jan 2019
Key Concept: Siteless
No physical site visits at all
Consent via app
Telemedicine for consultations
ECG patch mailed to participants
Primary Outcomes: (1) % of notified participants with AFib on ECG patch (2) Positive predictive value of irregular tachograms

## Slide 5
TECHNICAL APPROACH
5 / 12
How the Detection Algorithm Works
PPG Sensor
Green LED + light sensor
on Apple Watch.
Measures blood flow
changes at the wrist.
►
Tachogram
1-minute recording of
pulse intervals.
Passive, intermittent,
while user is at rest.
►
Classification
Algorithm checks if
pulse intervals are
regular or irregular
based on variability.
►
Multi-Confirm
Requires MULTIPLE
irregular tachograms
before issuing a
notification.
►
Notification
User gets one alert.
Subsequent data is
recorded but NOT
shown to user.
Key Design Choice: Single tachogram PPV = 0.71 → After multi-confirmation, notification PPV = 0.84. Requiring multiple irregular readings before alerting the user significantly reduces false alarms.

## Slide 6
TECHNICAL APPROACH
6 / 12
After the Notification: Verification Pipeline
1
Irregular Pulse Notification
Sent via app to user
▼
2
Telemedicine Visit #1
Physician confirms eligibility, checks for urgent symptoms
▼
3
ECG Patch (ePatch) Mailed
Worn up to 7 days, records continuous ECG
4
Patch Returned & Read
Two clinicians independently read; committee resolves disagreements
▼
5
Telemedicine Visit #2
Results discussed; participant directed to follow-up care
▼
6
90-Day Follow-up Survey
Did you see a doctor? New medications? New diagnosis?
►
Attrition: 2,161 notified → 945 completed visit → 658 shipped patch → 450 returned analyzable patch (20.8%)

## Slide 7
KEY RESULTS
7 / 12
Result 1: Who Got Notified?
0.52%
of all participants received
an irregular pulse notification
Notification Rate by Age
≥ 65 yr
3.14%
55-64 yr
1.3%
40-54 yr
0.37%
22-39 yr
0.16%
Our Take
The low notification rate (0.52%) shows the algorithm is deliberately conservative — it prioritizes not bothering users unnecessarily over catching every case. This is a design choice, not a flaw. But it also means we cannot know how many true AFib cases were missed (no sensitivity data). The study was not designed to answer that question.
Concept: Sensitivity vs. PPV
Sensitivity = of all people who truly have AFib, how many did the watch catch? (Not measured here)
PPV = of all people the watch flagged, how many actually had AFib? (This is what the study measures)

## Slide 8
KEY RESULTS
8 / 12
Result 2: Did the Notifications Find Real AFib?
34%
of notified participants had
AFib confirmed on ECG patch
(153 / 450, 97.5% CI: 29–39%)
Does 34% mean 66% were false positives?
No. The authors explicitly address this:
• ECG patch was applied on average 13 days after notification
• AFib is often paroxysmal — the episode may have ended by then
• 34% is a floor estimate, not a ceiling on true positives
• Among confirmed AFib: 89% had episodes lasting ≥ 1 hour
Concept: Confidence Interval (CI)
"97.5% CI: 29–39%" means: if we repeated this study many times, 97.5% of the time the true value would fall between 29% and 39%. Wider CI = more uncertainty, narrower CI = more precision.
Our Take
Only 450 out of 2,161 notified participants (20.8%) returned an analyzable ECG patch. The authors note that baseline characteristics were similar between those who returned patches and those who didn't. But we cannot be certain the 34% yield generalizes to the 80% who did not return patches — their AFib status is simply unknown.

## Slide 9
KEY RESULTS
9 / 12
Result 3: How Accurate Were the Alerts?
Single Tachogram
PPV = 0.71
97.5% CI: 0.69 – 0.74
71% of individual irregular
readings matched AFib on ECG
►
After Multi-Confirmation
PPV = 0.84
95% CI: 0.76 – 0.92
84% of notifications
were confirmed as AFib
What about the irregular readings that weren't AFib?
Of 600 irregular tachograms without AFib on simultaneous ECG:
77% — frequent premature atrial contractions (PACs)
38% — atrial tachycardia
16% — frequent premature ventricular contractions (PVCs)
Only 4.7% — sinus arrhythmia alone (truly "nothing wrong")
Our Take: Even when the algorithm "got it wrong," it was mostly detecting real cardiac abnormalities — not noise. Only ~5% were truly benign. The clinical significance of these non-AFib findings (PACs, PVCs) deserves further study.

## Slide 10
KEY RESULTS
10 / 12
Result 4: Did Notifications Change Behavior?
57%
contacted a healthcare
provider outside the study
28%
were prescribed
new medication
33%
were recommended
to see a specialist
76%
contacted some form
of medical provider
End-of-Study: 44% of notified participants reported a new AFib diagnosis vs. only 1.0% of non-notified participants
Safety: 1,038 adverse events reviewed. 16 app-related (15 were anxiety). No serious app-related adverse events.

## Slide 11
LIMITATIONS & OPEN QUESTIONS
11 / 12
What This Study Cannot Tell Us
No Sensitivity / Specificity
By design. Only PPV was measured.
We don't know how many true AFib
cases the watch missed.
Authors state this
Low ECG Patch Return Rate
Only 20.8% returned patches.
34% yield may not generalize
to the other 80%.
Authors state this
Self-Reported Eligibility
Some notified participants later
reported prior AFib history.
No clinical verification at enrollment.
Authors state this
Population Skew
Mean age 41, 68% white.
Reflects Apple Watch owners,
not the high-risk AFib population.
Authors state this
No Clinical Hard Endpoints
Proves detection, not outcomes.
Does earlier detection reduce
stroke or mortality? Unknown.
Not addressed
PPG & Skin Tone
PPG signal quality varies with
skin pigmentation. 81% of notified
group was white. No subgroup analysis.
Not addressed
Authors state this = acknowledged in the paper Not addressed = our observation, outside the paper's scope

## Slide 12
12 / 12
Key Takeaways
✓
The watch's notification algorithm has a PPV of 0.84 — when it alerts, it's usually right.
✓
Only 0.52% of users were notified — the algorithm is conservative by design.
✓
34% of notified participants had AFib confirmed on ECG. This is a floor, not a ceiling.
✓
Notifications drove real clinical action: 57% saw a doctor, 28% got new prescriptions.
What Remains Open
?
Does detecting AFib earlier actually reduce stroke, death, or disability? (Needs RCTs)
?
How does the algorithm perform across diverse skin tones and age groups?
?
If this becomes a consumer feature — who is liable for a missed or false diagnosis?
?
How should FDA regulation adapt to consumer-grade medical monitoring tools?